## Slide 1: Verilog: Multicore CPU – Matrix Multiplication
Name: Vòng Chí Cường
MSSV: 21521910
TA: Hồ Ngọc Diễm

## Slide 2: Introduction Algorithm 01 02 ISA & Modules Results Analyzing and Verification 03 04 Table of contents

## Slide 3: Introduction 01
You can enter a subtitle here if you need it

## Slide 4: Process overview
0
Create random matrices to multiply
01
Convert it to binary stream
10
Implement assembly code for the algorithm to multiply 2 matrices
11
100
101
110
Send the data to the data memory and instruction memory of the system in the FPGA board (via UART)
Matrix multiplication using multi-core processor
Send the answer matrix as a binary data stream to the laptop
Convert binary data to answer matrix
111
Validate the calculation

## Slide 5: Processor design flow
0
Design a matrix multiplication algorithm
01
Design the ISA
10
Design the (primitive) Data Path
11
100
101
110
Design the Assembly code
Design the Micro-Architecture
Extend processor design to multi-core processor design
Implement Communication system between FPGA board and the laptop

## Slide 6: Algorithm 02

## Slide 7: PesudoCode with one Core
Algorithm :
Initialization:
a <- row_P; b <- column_P(row_Q); c <- column_Q;
RP <- start_P, RQ <- start_Q
Mem[6] <- end_P, Mem[7] <- end_Q
Mem[8] <- start_P, Mem[9] <- start_Q, Mem[10] <- start_R
AC, R, RC <- 0
for i = 0; i < a; i ++;
for j = 0; j < c; j ++;
output_value = 0;
for count = 0; count < b; count++;
output_value+ = matrixP[i][count] × matrixQ[count][j];
save matrixR[i; j] <- output_value;

## Slide 8: ISA & Modules 03

## Slide 9: Top Modules

## Slide 10: Instruction Set
INSTRUCTION | OPCODE | OPERATION
NOP | 0 | No operation
ENDOP | 1 | End operation
CLAC | 2 | AC 0
LDIAC | 3 | AC dataMemfaddrg
LDAC | 4 | AC dataMemfACg
STR | 5 | dataMemfACg R
STIR | 6 | dataMemfaddrg R
JUMP | 7 | PC instructionMemfaddrg
JMPNZ | 8 | Jump if z!=0
JMPZ | 9 | Jump if z==0
MUL | 10 | AC AC*R1
ADD | 11 | AC AC+R
SUB | 12 | AC AC-RC
INCAC | 13 | AC AC+1
MV RL AC | 14 | RL AC
MV RP AC | 15 | RP AC
MV RQ AC | 16 | RQ AC
MV RC AC | 17 | RC AC
MV R AC | 18 | R AC
MV R1 AC | 19 | R1 AC
MV AC RP | 20 | AC RP
MV AC RQ | 21 | AC RQ
MV AC RL | 22 | AC RL

## Slide 11: Memory Locations of Some Necessary Data Values
0 | a | No. of rows of matrix P
1 | b | No. of columns of matrix P (No. of rows of matrix Q)
2 | c | No. of columns of matrix Q
3 | start addr P | Start address of matrix P
4 | start addr Q | Start address of matrix Q
5 | start addr R | Start address of matrix R
6 | end addr P | End address of matrix P
7 | end addr Q | End address of matrix Q
8 | current addr P | The address of currently processing data of matrix P
9 | current addr Q | The address of currently processing data of matrix Q
10 | current addr R | The address of currently processing data of matrix R
11 | current c | Current row count
12 | current a | Current column count

## Slide 12: Datapath of CPU

## Slide 13: Micro-instructions

## Slide 14: State Diagram

## Slide 15: Summary of Verilog

## Slide 16: What is “gotcha” ?
Definition
Examples
A programming "gotcha" is a language feature, which, if misused, causes unexpected-and, in hardware design, potentially disastrous-behavior

## Slide 17: Gotcha In hardware design and verification, most gotchas will simulate, but give undesired results
Gotchas can be difficult to find and debug 
A gotcha can be disastrous if not found before tape-out!

## Slide 19: Case sensitivity
Verilog and SystemVerilog are case-sensitive languages, meaning that lowercase letters and uppercase letters are perceived as different in identifiers and in keywords.
Keywords are always in all lowercase letters

## Slide 20: Implicit Net Declarations
Implicit nets can save typing hundreds of lines of code in a large, gate-level design.
But…
An undeclared vector connection infers a 1-bit wire, not a vector;
A typographical error in a netlist becomes a functional bug
An undeclared signal used in a netlist infers an implicit net

## Slide 21: Implicit Net Declarations

## Slide 22: Programming Gotcha Default Base of Literal Numbers is Decimal
Optionally, literal numbers can be defined with a base
’hC // unsized hex value
2’b01 // sized binary value

## Slide 23
Gotcha: My combinational logic seemedto simulate OK, but aftersynthesis, thegate-level simulation does notmatch the RTLsimulation.
Synopsis: If combinational logic calls a function, then the combinational sensitivity list must include signals that thefunction reads. @* does not infer sensitivity to values readbyfunctions calledfrom combinational logic
Combinational logic sensitivity lists with function calls

## Slide 24: We find solutions…
Using @*
The @* wildcard will automatically be sensitive to any nets or variables that are read in the always procedural block, including any nets or variables that are passed to a function input.

## Slide 25: We find solutions…
However, @* has a subtle gotcha that is not widely known. It only infers sensitivity to signals directly referenced in the always block. It will not infer sensitivity to signals that are externally referenced in a function that is called from the always block. That is,the @* will only be sensitive to thesignals passed into the function or task.
module MyModule(input wire a, input wire b, output wire c);
always @* begin
c = myFunction(a, b);
end
function logic myFunction(input wire x, input wire y);
logic result;
// Some logic using x and y
// ...
return result;
endfunction
endmodule

## Slide 26: Operation Size and Sign Extension Self-determined operators : do not modify their operand(s)

## Slide 27: Operation Size and Sign Extension
Context-determined operators : modify all operands to have the same size, using zero-extension or sign-extension

## Slide 28: References Verilog and SystemVerilog Gotchas 101 Common Coding Errors and How to Avoid Them --- Verilog and SystemVerilog Gotchas: 101 Common Coding Errors and How to Avoid Them | SpringerLink
Standard Gotchas Subtleties in the Verilog and SystemVerilog Standards That Every Engineer Should Know
--- Standard Gotchas (lcdm-eng.com)

## Slide 29: Thank you for watching